## Slide 1: Software and Energy-aware Computing Fundamentals of static analysis of software
John Gallagher
Roskilde University
ICT-Energy: Energy consumption in future ICT devices
Summer School, Aalborg, Denmark, August 13-16, 2016

## Slide 2: Acknowledgements
The partners in the EU ENTRA project (2012-2015)
Kerstin Eder and team
Pedro López García and team
Henk Muller and team
Roskilde team
http://entraproject.eu

## Slide 3: Whole-systems energy transparency
Physics
Application Software
System Software
Architecture
Devices
Energy is consumed by physical processes.
Yet, application programmers should be able to “see” through the layers and understand energy consumption at the level of code.
The same applies to designers at every level.
How is this possible?

## Slide 4: Energy of software?
Energy is consumed by hardware
But in these lectures we attribute energy cost to software
Why?
  (to summarise some of Kerstin’s points)

## Slide 5: Reason 1
We take the application programmer’s viewpoint
  programmers don’t know much about hardware
  high-level languages hide the platform from the programmer
    Which is usually a Good Thing, don’t you agree?

## Slide 6: Reason 2
Energy efficiency as a design goal from the start
Get an energy profile for a program as early as possible
Analyse the code to find out how much energy a program will use
Deliver software with energy guarantees

## Slide 7: Reason 2 - continued
Don’t wait to test energy efficiency on hardware, after the software is developed
It might be too late to fix “energy bugs”
Development
machine
Deployment
platform

## Slide 8: Reason 3
You can save more energy at the software level than the hardware level
There are more energy optimisation opportunities higher up the system stack.
Most energy is wasted by application software

## Slide 9: Energy transparency
Our aim is to let the programmer “see” the energy usage of the code
  without executing it
  so that the programmer can “see” where the program wastes energy
  experiment with different designs

## Slide 10: Example
biquadCascade(BANKS)
=
157 * BANKS + 51.7
nJoules
This is an estimate of
the energy used by the
function.
It is a linear function of
the value of BANKS

## Slide 11: Visualise energy of program blocks

## Slide 12: Which code blocks are hot?

## Slide 13: Tiwari’s Energy Equation (from Kerstin’s slides)
13
Ni is the number of times instruction i is executed.
Ni,j is the number of times instruction i is followed by instruction j in the program execution.
Ni and Ni,j might depend on input data, so cannot be counted directly for all possible inputs
Notes: Short excurse into how this may be possible to do:
large loops of each instruction to determine the base costs
large loops of pairs of instructions to determine the switching costs
Which data should we use?

## Slide 14: Example

## Slide 15: Energy a design goal for programmers

## Slide 16: Summary of goals
Tools for the programmer
  that give information about the energy usage of programs without running them (energy transparency)
  that allow energy assertions to be checked (energy design goals)

## Slide 17: Semantics and program analysis
To achieve the goals we need tools for program analysis
Program analysis is based on formal program semantics
  the mathematical study of program meanings

## Slide 18: Programs are machines (that consume energy)
n = 4;
z = 1;
while (n > 0) {
z = z*n;
n = n-1;
}
print(z);
Semantics gives the “machine” defined
by a program.

## Slide 19: Software factors affecting energy
The main factors are
Computational efficiency
Quality of low-level machine code
Parallelism

## Slide 20: Computational efficiency
There is a strong correlation between time and energy consumption (for a single thread)
Execute as few instructions as possible to achieve the given task, saving energy
Furthermore, the machine will return more quickly to an idle (low-energy) state

## Slide 21: Computational efficiency (2)
Hence a large part of the energy-aware programmer’s job is the same as for performance-awareness
Get the job done quickly, using efficient algorithms and data structures

## Slide 22: Low-level code optimisation
Given the same high-level code (e.g. C++) there could be many different machine instruction programs.
Lower energy can be achieved e.g.
  using VLIW (Very Long Instruction Word) instructions and vectorisation
  exploitation of low-power processor states using frequency and voltage scaling (DVFS).

## Slide 23: Parallelism
Is it more energy-efficient to parallelise a task?
The answer is not straightforward.
Execution time might be reduced but more energy might be consumed
e
e1
e2
e3
e > e1 + e2 + e3 ???
If the processors for each process
are identical, then the parallel program
probably uses more energy.
There is some overhead for managing
threads and communication.
SEQ
PAR

## Slide 24: Parallelism and clock speed
Let f = processor clock frequency
Let P = power
Let V = voltage
P = cV2f (where c is a constant)
E = Pt (when we run the processor for t time units)
Hence e = e1 + e2 + ... + en for n processes, if the same total number of instructions is executed, at the same frequency f.
But if we reduce f, the total energy will reduce because V can also be reduced and P is proportional to V2!!!

## Slide 25: Parallelism (cont’d)
Hence it is worth parallelising for energy saving if
  there is little or no idle time in each processor
    a waiting processor is wasting energy
  the clock speed can be reduced in some or all processors, compared to a single process execution

## Slide 26: How can static analysis help?
Automatic complexity analysis
  understand the best, worst and average cases
  optimise hot loops
Timing and synchronisation analysis
  compare parallel algorithm performance, throughput, etc.
  identify wait times, potential low-power states, etc.

## Slide 27: Analysis of programs
A program is a physical object. e.g.
  some symbols on paper
  a pattern of bits in memory
But what is the meaning of a program?
This is program semantics.

## Slide 28: Program semantics
n = 4;
z = 1;
while (n > 0) {
z = z*n;
n = n-1;
}
print(z);
To execute or analyse
this program,
we need to understand
the meaning of teh symbols
such as “while”, “>”, “*”,
“;”, ”{”, “}”, etc.

## Slide 29: Different styles of program semantics
Operational semantics
  small steps (from one state to the next)
  big steps (from the start to the end state)
  Hoare-Floyd conditions
Denotational semantics
  the mathematical function represented by a program
  obtained by composing its parts

## Slide 30: Phases of semantic analysis
Syntax analysis (parsing)
  breaking the program into is basic parts and determining its structure
Semantic translation
  representation of the program in some suitable mathematical or logical form
Semantic interpretation
  using the semantic representation to analyse the program execution

## Slide 31: Program syntax tree (parsing)
n = 4
z = 1
z = z*n
n = n-1
print(z)
while
n>0
Statement List
Statement List
n = 4;
z = 1;
while (n > 0) {
z = z*n;
n = n-1;
}
print(z);

## Slide 32: From syntax tree to flow graph
n = 4
z = 1
z = z*n
n = n-1
print(z)
while
n>0
Statement List
Statement List
n = 4;
z = 1;
while (n > 0) {
z = z*n;
n = n-1;
}
print(z);
true
false

## Slide 33: From flow graph to state automata
n z
n’ z’
n = 4
z = 1
n > 0
n’ = n-1
z’ = z * n
n = n’
z = z’
n ≤ 0, print(z)
stop
start

## Slide 34: Exercise
while (m != n) {
if (m > n) {
m = m-n;
}
else {
n = n-m;
}
}
Draw the syntax tree
Draw the control flow graph
Draw the state automaton

## Slide 35: Phases of semantic analysis
Syntax analysis (parsing)
  breaking the program into is basic parts and determining its structure
Semantic translation
  representation of the program in some suitable mathematical or logical form
Semantic interpretation
  using the semantic representation to analyse the program execution

## Slide 36: From automaton to predicate logic
true → reachable1
(reachable1 ⋀ n=4 ⋀ z=1)
→ reachable2(n,z)
(reachable2(n,z) ⋀ n<0 ⋀ z’=z*n ⋀ n’=n-1)
→ reachable3(n’,z’)
(reachable3(n’,z’) ⋀ n=n’ ⋀ z=z’ )
→ reachable2(n,z)
reachable2(n,z) ⋀ n ≥ 0 ⋀ print(z) )
→ stop

## Slide 37: Logical representation
x1, x2, ..., xn
x’1, x’2, ..., x’n
e(x1, x2, ..., xn, x’1, x’2, ..., x’n)
program point j
program point k
(reachablej(x1, x2, ..., xn) ⋀ e(x1, x2, ..., xn, x’1, x’2, ..., x’n))
→ reachablek(x’1, x’2, ..., x’n)
transition constraint

## Slide 38: Example: A rate limiter*
*Example by Monniaux

## Slide 39: More examples from ENTRA tool

## Slide 40: Identification of basic blocks
A basic block is a section of “straight-line” code.
  The start of a block is a branch or merge point
  The end of a block is a branch or jump
Basic blocks can be extracted from the control flow graph
Every statement in a basic block is executed the same number of times

## Slide 41: Rate limiter – logic representation
r1(X,X_old) :-
X_old=0,
r0(_,_).
r1(X,X_old) :-
r5(X,X_old).
r2(X,X_old) :-
X >= -1000,
X =< 1000,
r1(_,X_old).
r3(X,X_old) :-
X1 >= X_old+1,
X = X_old+1,
r2(X1,X_old).
r3(X,X_old) :-
X < X_old+1,
r2(X,X_old).
r4(X,X_old) :-
X1 =< X_old-1,
X = X_old-1,
r3(X1,X_old).
r4(X,X_old) :-
X > X_old-1,
r3(X,X_old).
r5(X,X_old) :-
X_old=X,
r4(X,_).

## Slide 42: Phases of semantic analysis
Syntax analysis (parsing)
  breaking the program into is basic parts and determining its structure
Semantic translation
  representation of the program in some suitable mathematical or logical form
Semantic interpretation
  using the semantic representation to analyse the program execution

## Slide 43: Program analysis
Program properties
Program invariants
Global properties that depend on summary of an infinite number of behaviours
Prove absence of bugs (verification) rather than presence (testing)

## Slide 44: Invariants
Many program analysis and verification tasks involve proving invariants
An invariant is an assertion that is true at a given program point.

## Slide 45: Example invariant
-1000 ≤ x_old ≤ 1000
Check assertion

## Slide 46: Proving invariants
To prove that invariant P holds at program point j, prove the following implication
  reachablej(x1,...,xn) → P
  which is equivalent to
  ¬( reachablej(x1,...,xn) ⋀ ¬P)

## Slide 47: Proof by approximation
reachablej(x1,...,xn)
P
Overapproximation
of the set of points
where
reachablej(x1,...,xn)
is true.
Contained
within P, hence
reachablej(x1,...,xn)→P

## Slide 48: Energy invariants
The program state can contain resource counters.
reachablek(x1,...,xn,e) means that the total energy consumed is e, when the program reaches point k
So we can express and prove assertions about energy (or other resources)
More on this later...

## Slide 49: Two basic techniques
How to capture all reachable states?
  answer, fixpoint techniques
How to capture an infinite set of states?
  answer, abstract interpretation
These two methods underlie much program analysis

## Slide 50: Fixpoint computation
Sounds complicated, but it is a very simple procedure
It is a closure or saturation procedure

## Slide 51: Fixpoint example
Consider a route network, with stations a,b,...,h
a
c
b
d
e
g
f
h

## Slide 52: post(S) function
Let S be a set of stations.
post(S) is the set of stations reachable in one step from S. E.g. post({a,h}) = {b,c,d,g}
a
c
b
d
e
g
f
h

## Slide 53: Reachability as a fixpoint
The set of stations reachable from an initial set S, called Reach(S) is defined as the smallest set Z such that Z = F(Z)
  where F(Z) = S ∪ post(Z)
This can be computed as the limit of a sequence ∅, F(∅), F(F(∅)), ...

## Slide 54: Example
Find the stations reachable from a.
a
c
b
d
e
g
f
h
F(Z) = {a} ∪ post(Z)
∅
F(∅) = {a}
F({a}) = {a,b,c,d}
F({a,b,c,d}) = {a,b,c,d,f}
F({a,b,c,d,f}) = {a,b,c,d,e,f}
F({a,b,c,d,e,f}) = {a,b,c,d,e,f}
fixpoint found {a,b,c,d,e,f}

## Slide 55: Exercise
Using the same graph, compute the set of states reachable from e, using a fixpoint computation.

## Slide 56: The reachable states of a program
We apply the same idea to find the reachable states of a program, starting with the initial state.
n z
n’ z’
n = 4
z = 1
n > 0
n’ = n-1
z’ = z * n
n = n’
z = z’
n ≤ 0, print(z)
stop
start

## Slide 57: The reachable states of a program
n z
n’ z’
n = 4
z = 1
n > 0
n’ = n-1
z’ = z * n
n = n’
z = z’
n ≤ 0, print(z)
stop
start
2
3
2 3
{} {}
{(4,1)} {}
{(4,1)} {(3,4)}
{(4,1),(3,4)} {(3,4)}
{(4,1),(3,4)} {(3,4),(2,12)}
.... ....
{(4,1),(3,4), {(3,4),(2,12),(1,24)}
(2,12),(1,24),
(0,24) }
(n,z) represents the values of n and z at a given point

## Slide 58: Infinite fixpoints
However, usually the set of reachable states of a program is infinite, and the sequence could keep on growing
We might never reach the fixpoint
In this case we use abstraction

## Slide 59: Abstract interpretation
Example
476305 × -576 = 274351680
Is the above equation correct?

## Slide 60: Rule of signs
The rule of signs is an abstraction of the multiplication relation
  + × + = +
  + × − = −
  − × + = −
  − × − = +
  We can check incorrectness, but not correctness with the rule of signs.

## Slide 61: The interval abstraction
The value of a variable is abstracted by an interval
  The variable has any value within the interval
We can perform operations on intervals, as we did for signs
E.g. [3,10] + [-2,6] = [3+(-2), 10+6] = [1,16]
Exercise. What is [3,10] − [-2,6]?

## Slide 62: Example: interval abstraction
The set of pairs of values {(4,1),(3,4), (2,12),(1,24),(0,24) } can be abstracted by the pair of intervals ([0,4], [1,24])
So n is between 0 and 4, z is between 1 and 24.
But information has been lost
  the pair (3,19) is also consistent with the intervals.
  the intervals give an over-approximation of the reachable states.

## Slide 63: Convex polyhedra
A more precise abstraction than intervals is given by convex polyhedra
Convex polyhedra are linear inequalities among the state variables

## Slide 64: Example convex polyhedron abstraction
r1(I,J) :-
I=0,J=10.
r2(I,J) :-
r1(I,J).
r2(I,J) :-
I1 =< J1,
I = I1+2,
J = J1-1,
r2(I1,J1).
r3(I,J) :-
I >= J+1,
r2(I,J).

## Slide 65: Approximate reachable states
r1(I,J) = [I=0,J=10].
r2(I,J) = [-I >= -16,I >= 0,I+2*J=20].
r3(I,J) = [-3*I >= -26,3*I >= 22,I+2*J=20].
This result is computed fast, using the
Parma Polyhedra Library to perform the
operations on convex polyhedra.

## Slide 66: Summary so far....
We can translate a program to a state automaton
We can compute over-approximation of the reachable states of the program
  using fixpoint computation and abstraction
We can use the approximation to check assertions about the program.

## Slide 67: Software and Energy-aware Computing Static analysis and optimization
John Gallagher
Roskilde University
ICT-Energy: Energy consumption in future ICT devices
Summer School, Aalborg, Denmark, August 13-16, 2016

## Slide 68: Energy models – block-based
n z
n’ z’
n = 4
z = 1
n > 0
n’ = n-1
z’ = z * n
n = n’
z = z’
n ≤ 0, print(z)
stop
start
LLVM block
ISA block
ISA energy model
eISA
eLLVM
[e1,e2]

## Slide 69: Adding energy to the model
n z e’
n’ z’ e
n = 4
z = 1
n > 0
n’ = n-1
z’ = z * n
n = n’
z = z’
n ≤ 0, print(z) e = e’+107
e
e
e = 0
e is an “energy counter”
e’ = e+17
e = e’+42
e’ = e+3
On each transition, increment the
energy counter by the amount of
energy required to execute the transition.
The numbers are obtained from a model

## Slide 70: Estimating total energy
The total energy consumed by the program is given by the energy counter in the reachable “stop” state.
For this example, the analysis yields a value of 304 (initial value n=4)
However if the input data is unknown, we would get a relationship between input value n and energy e.
In the example, e = 17 + n*45 + 107

## Slide 71: Beyond linear energy estimates
With polyhedron or interval abstractions, we are limited to linear expressions.
This is quite restrictive and approximate
A better approach is given by deriving cost functions from the automaton, and solving them

## Slide 72: Deriving cost functions
n z
n’ z’
n = ?
z = 1
n > 0
n’ = n-1
z’ = z * n
n = n’
z = z’
n ≤ 0, print(z)
stop
start
1
3
2
4
Let cost2(n) be the cost of
the loop starting at 2.
We can write a recurrence relation
cost2(n) = cost2(n-1) + 45 (if n > 0)
cost2(n) = 0 (if n ≤ 0)
The cost of the whole computation
for input n is 17 + cost2(n) + 107

## Slide 73: Solving cost relations
Tools like Mathematica are capable of solving many recurrence relations.
  cost2(n) = cost2(n-1) + 45 (if n > 0)
  cost2(n) = 0 (if n ≤ 0)
  has a closed-form solution
  cost2(n) = 45*n

## Slide 74: More complex cases
By solving energy recurrence equations we can get non-linear energy functions
E.g. a matrix multiplication program for matrices of size n
  42.47 n3 + 68.85 n2+ 49.9 n + 24.22 nJoules

## Slide 75: Some available tools for cost analysis
CiaoPP (IMDEA Software, Madrid)
  a resource analysis tool based on solving cost relations (using Mathematica)
  designed for Prolog programs, adapted to imperative languages
COSTA (UCM, Madrid).
  Can analyse resources such as time and energy for Java and Java bytecode (uses the PUBS solver)
Termination analysis tools
  several tools for proving termination of programs are being adapted for resource analysis

## Slide 76: Trickier examples
Loops counters can have inter-dependencies
Complexity of example is O(2.m), not O(m2)
void main(int m) {
int i=m, n = 0; //stack = emptyStack();
l1 : while (i > 0) {
i--;
if (?) //push
n++; //stack.push(element);
else //popMany
l2 : while (n > 0 && ?)
n--; //element = stack.pop();
}
}

## Slide 77: Analysis of communication and timing
We consider a language with synchronous channel communication
Usually, threads enter some periodic behaviour, synchronising among themselves
The programmer needs a model of how much work and time a thread uses between communications

## Slide 78: Potential power optimisations (1)
Sometimes, threads should run as slowly as possible, while still meeting deadlines from other threads
  thus analysis of timing and synchronisation is critical
Reducing clock frequency of cores saves power

## Slide 79: Potential power optimisations (2)
Threads that communicate a lot should be close (take account of communication infrastructure).
Bottlenecks can be removed by shifting tasks or introducing more threads
Very inactive threads can be merged with other threads.

## Slide 80: Parallel execution
The threads run
until they reach a
synchronisation point.
After synchronising, they
continue to the next, etc.
Timing analysis is vital.
The left thread always
waits for the other.
Possible energy
optimisations:
1. slow down the left
thread
2. give it some more work
to balance the load
3. put in power-saving
mode while waiting

## Slide 81: Behaviour of a single thread
Communication-free code
Communication-free code
Communication-free code
Communication-free code
fork
comm
comm
comm
comm
join
Each thread is parsed into blocks of communication-free code, separated
by synchronous communications.
Assume that the communication channels are staticallly known.

## Slide 82: Example thread behaviour
P
R
Q
S
4
b
c
d
g
f
e
h
1
a
2
3
5
6
7
8
8 threads in a pipeline with a split in the middle.
P,Q,R and S are some functions on the values passed along.

## Slide 83: Analysis of the sequential components
We assume that we used the sequential techniques already mentioned
  to get energy estimates for P,Q,R and S
  to get execution time estimates for P,Q,R and S

## Slide 84
A1
A2
start
a
a
H1
H2
start
h
h
B1
B2
start
a
a
P
b
E1
E2
start
d
R
f
D1
D2
start
c
c
Q
e
G1
G2
start
g
g
S
h
C1
C5
start
b
b
C2
b
C3
C4
c
d
F1
F5
start
e
e
F2
f
F3
F4
g
g
d
Automata for the individual threads

## Slide 85: Energy and power estimates
The energy of the whole cycle consists of
  the total energy for the tasks in the cycle
  an overhead for the number of active threads (obtained from the critical path)
  an estimate of the energy used while idling
The power (Watts) is E/T, where E is the energy and T is the time of the cycle

## Slide 86: Task durations
Assume that each task has a duration
  could be an interval [lower, upper]
  or in general a constraint that could depend on data values
  these can be obtained from a timing analyser and/or automatic complexity analysis
  Let the duration of Task k be dk

## Slide 87: Synchronisation
Task 1
Thread 1
Thread 2
Task 2
Task 4
Task 3
channel c
Tasks 2 and 4
can start simultaneously as soon as both Tasks 1 and 3 have completed and the channel communication has been made.

## Slide 88: Synchronisation constraints (1)
Task 1
Thread 1
Thread 2
Task 2
Task 4
Task 3
channel c
n ≥ 0, m ≥ 0
t2n = max(t1n + d1, t3m + d3)
t2n = t4m
If Task 2 (or 4) is a loop header
then replace t2n (or t4m)
with t2n+1 (or t4m+1)
loop counter n
loop counter m
Let tkm be the time of the mth
firing of task k.
(Inspired by SDF graphs)

## Slide 89: Counting communications
T0
Tm
start
a(0)
T1
b(1)
Let cpre be the number of channel communications on c in the loop prefix.
Number every channel communication,
for each channel c in the loop
c(1), ... c(k)
cpre + n * k + j = the number of communications on c when
c(j) in the loop is encountered, when n iterations of the loop are completed.
b(2)
a(1)
a(k)
Annotate the channel communications
so that they can be counted.
loop
prefix
loop

## Slide 90: Synchronisation constraints (2)
Task 1
Thread 1
Thread 2
Task 2
Task 4
Task 3
channel c
On a channel c, there is the same number of operations at each channel end.
cpre1 + n*k1 + j
cpre2 + m*k2 + i
=
loop counter n
loop counter m
We assume that each channel joins exactly two threads.

## Slide 91: Example (logical encoding)
fires__B2(A,5+B) :-
1+C*2+1=0+A*1+1,
1+C*2+1>=0,
C>=0,
A>=0,
fires__C2(C,B),
fires__G(A,D),
5+B>=300+D.
fires__B2(A,300+B) :-
1+C*2+1=0+A*1+1,
1+C*2+1>=0,
C>=0,
A>=0,
fires__C2(C,D),
fires__G(A,B),
5+D<300+B.
B1
B2
start
a
a
G
b
C1
C5
start
b
b
C2
b
C3
C4
c
d
A and C are the loop counters og G and C2
300
5

## Slide 92: Analysis of the constraints
Generate the complete set of synchronisation constraints
Solve them
  more generally, obtain an approximate solution (abstract interpretation again!)
For each task, derive a relationship between n and t, where t is the task’s nth firing time.

## Slide 93: Transient and periodic behaviour
Typically, threads take a few iterations to reach a steady state.
t
n
First few firings
happen rapidly,
then there is a slowdown as delays from other threads take effect.

## Slide 94: Approximation of throughput
t
n
Approximation using a finite union of convex polyhedra

## Slide 95: Analysis results
For the 8-thread pipeline example
Given task durations
  G = 300
  Q = 334
  R = 500
  S = 250
  all other tasks = 5
Derive period of threads = 610 or 305
Some threads loop twice as fast as others

## Slide 96: Thread activity
Thread 1 = 5/305 (1.6%)
Thread 2 = 305/305 (100%)
Thread 3 = 20/610 (3.2%)
Thread 4 = 339/610 (56%)
Thread 5 = 505/610 (83%)
etc.
A
B
C
E
D
F
G
H
a
b
c
d
f
e
g
h
300
500
334
250

## Slide 97: Other information
Throughput and thread activity obtained directly from the solution to the constraints
Other information that can be derived from earliest firing time includes
  when one task definitely waits for another
  which tasks can run simultaneously
  which tasks on different threads do not run at the same time
  frequency of each channel communication

## Slide 98: Energy and power estimates
The energy of the whole cycle consists of
  the energy for each task in the cycle
  an overhead for the number of active threads (obtained from the critical path)
  an estimate of the energy used while idling
The power (Watts) is E/T, where E is the energy and T is the time of the cycle

## Slide 99: Possible transformations
A
B
C
E
D
F
G
H
A
B
C
E
D
F
G
H
c
f
B
G
A
B
C
E
D
F
G
H

## Slide 100: Energy model and optimisation for Android
Android code is Java
What is the code’s energy cost

## Slide 101: Which code blocks use most energy?
A few blocks dominate energy usage. These are targets for energy optimisation

## Slide 102: Optimisation. Example 1
Energy consumption of the code without and with the
changes in Click & Move.
Overall saving:
6.4%

## Slide 103: Optimisation. Example 2
Energy consumption of the code without and with the
changes in Orbit.
Overall saving:
50.2%

## Slide 104: Energy optimisations through energy transparency
A thorough energy analysis of a suite of code enabled insight into where most energy was consumed
This enabled source-code transformations to be focussed on the most effective areas.

## Slide 105: Energy optimisation for Android game code case study
Work by Xueliang Li, Roskilde University (to appear in SCAM 2016)
Energy of game code is highly dependent on user interaction
We modelled the energy consumption the Cocos2d-Android game engine
Energy consumption of operations in the source code was estimated using machine learning techniques
  based on a large number of test cases for different interaction scenarios.

## Slide 106: Identifying which ops use most energy
Top 10 ops
account for
72.1% of
energy usage

## Slide 107
Thank you