## Slide 1
Department of
COMPUTER SCIENCE
Software and
energy aware computing
Kerstin Eder
Design Automation and Verification, Microelectronics
Verification and Validation for Safety in Robots, Bristol Robotics Laboratory

## Slide 2: Bristol

## Slide 3: The University of Bristol
UoB founded in 1909
  The first higher education institution in England to admit women on an equal basis to men. 
Top 30 universities globally
(QS World University Rankings)
6 Faculties
~14.000 students, 2.000 in FEN
Computer Science in FEN
EACO workshops and research to advance the state of the art in Energy Aware COmputing
Notes: EACO funded by University Strategy fund and Institute for Advanced Studies

## Slide 4
Department of
COMPUTER SCIENCE
Software and
energy aware computing
Kerstin Eder
Design Automation and Verification, Microelectronics
Verification and Validation for Safety in Robots, Bristol Robotics Laboratory
More power to software developers!
Notes: Why we should give “more power” to SW developers.
Are there any SW developers here today?

## Slide 5: Overview
Introduction and Motivation
  Energy consumption of Computing
  Software vs Hardware

## Slide 6: Overview
Introduction and Motivation
  Energy consumption of Computing
  Software vs Hardware

## Slide 7: Overview
Introduction and Motivation
  Energy consumption of Computing
  Software vs Hardware
  Energy Transparency
Measuring the energy consumption of software
  Demonstration with hands-on session by Steve Kerrison
Energy modeling
Fundamentals of static analysis of software
Static analysis and optimization

## Slide 8: Learning Objectives
Why software is key to energy efficient computing
What energy transparency means and why we need energy transparency to achieve energy efficient computing
How to measure the energy consumed by software
How to estimate the energy consumed by software without measuring
How to construct energy consumption models

## Slide 9: Introduction and Motivation
Pictures taken from the Energy Efficient Computing Brochure at: https://connect.innovateuk.org/documents/3158891/9517074/Energy%20Efficient%20Computing%20Magazine?version=1.0

## Slide 10
Pictures taken from the Energy Efficient Computing Brochure at: https://connect.innovateuk.org/documents/3158891/9517074/Energy%20Efficient%20Computing%20Magazine?version=1.0
Notes: Whether embedded systems, mobile devices, or the large-scale systems that help predict the weather

## Slide 11
Pictures taken from the Energy Efficient Computing Brochure at: https://connect.innovateuk.org/documents/3158891/9517074/Energy%20Efficient%20Computing%20Magazine?version=1.0
Notes: Energy efficiency is the limiting factor in system design.
Energy has become the primary limiting factor in the development of all systems, whether due to the cost of energy or cooling in large systems or due to battery life in mobile devices.

## Slide 12: Electricity Consumption (Billion kwH, 2007)
UK
Greenpeace’s Make IT Green Report, 2010.
http://www.greenpeace.org/international/en/publications/Campaign-reports/Climate-Reports/How-Clean-is-Your-Cloud/
UK
Cloud computing
Notes: More than 10% of the world’s energy consumption is spent on computing.
IT creates 50% more CO2 than the aviation sector. (2014)
Cloudland is the 5th largest consumer of electricity – consuming almost twice as much as the UK!
http://www.vertatique.com/ict-10-global-energy-consumption
http://www.vertatique.com/what-attached-our-global-ict-infrastructure

## Slide 13
“Despite improved energy efficiency, energy consumption through electronic devices will triple until 2030 because of a massive rise in overall demand.”
13
Notes: Predictions suggest that energy consumption through electronic devices will TRIPLE until 2030

## Slide 14: Crowds in St. Peter’s Square
http://www.spiegel.de/panorama/bild-889031-473266.html
2005
2013
Notes: In less than 10 years the same scene looks very different.
Since 2014 the number of electronic devices has more than doubled – being estimated at 19 Billion at the moment.
There are officially more mobile devices than people in the world 2014 – 7.2 Billion.
Estimates now 19 Billion.

## Slide 15: Energy Aware Computing
Notes: This calls for Energy Aware System Design

## Slide 16: Energy Efficiency of ICT
gAtes
Blocks
arChitecture
http://www.clker.com/cliparts/f/0/5/1/12937499341853355695circuit-board.jpg
Notes: Low power has been the focus for hardware developers for more than a decade with great success.

## Slide 17
A historical perspective
(based on an inspiring talk by Steve Furber)

## Slide 18: The Baby (1948)
filled a medium-sized room
executed
700 instructions per second
Notes: So, how did we get all this technology?
The first modern computer – the first computer to run a program stored in its memory – was the Manchester baby machine, built in Manchester. It ran the world’s first computer program in June 1948.
3 bit instruction encoding with 32-bit word length and a memory of 32 words
This is a photo of a replica of the Baby, built for the 50th anniversary of the first program, and now a permanent exhibit in the Museum of Science and Industry.
---
The Manchester Small-Scale Experimental Machine (SSEM), nicknamed Baby, was the world's first stored-program computer. It was built at the Victoria University of Manchester, England, by Frederic C. Williams, Tom Kilburn and Geoff Tootill, and ran its first program on 21 June 1948.

## Slide 19: The ARM968 (2005)
fills 0.4mm2 of silicon
executes 200,000,000 instructions per second
~300,000 times more than the Baby!
4mm
2.5mm
Notes: The ARM968E-S is a fully synthesizable 32-bit RISC processor aimed specifically at embedded real-time applications, and is the smallest, lowest power ARM9 family processor.
About 50 years later technology had moved on. This is a photo of a telecommunications controller, the processing part of which was developed by Steve Furber in Manchester.
It’s pretty typical of the sort of chip that is going into a whole lot of today’s low-power, mobile computing systems.
A comparison of Baby with ARM968 illustrates some interesting points…

## Slide 20: ~60 years of progress
Baby, 1948:
  filled a medium-sized room
  used 3.5 kW of electrical power
  executed 700 instructions per second
ARM968, 2005:
  fills 0.4mm2 of silicon (130nm)
  uses 20 mW of electrical power
  executes 200,000,000 instructions per second
Notes: In just 50 years computers have gone:
- from filling a room to fitting on a fingernail;
- from using a large mains supply to running for hours of small batteries;
- from executing a few hundred instructions a second to executing tens or hundreds of millions a second

## Slide 21: Energy efficiency
Baby:
  5 Joules per instruction
ARM968:
  100 pico Joules per instruction
(James Prescott Joule born Salford, 1818)
Notes: We can some idea of the relative efficiencies of these two machines by comparing their “fuel efficiency”. In the case of a computer, this is the energy taken to execute one instructions.
Baby consumed about 5 Joules per instruction;
DRACO consumes a whole lot less, namely 100pJ
The ratio of these two numbers is over 2 billion (in fact, 50 billion), which is one of these numbers that comes up in computing technology that is very hard to get a feel for.
If cars had improved by a similar ratio in their fuel efficiency, a few gallons of petrol would be enough to keep the UK mobile for a year, and the oil crisis would be forgotten.
However, there are, of course, good reasons why cars cannot achieve such levels of fuel efficiency. Whereas there is no lower limit to the fuel efficiency of computing – it can, at least in theory, be done with no energy at all…

## Slide 22: Energy efficiency
Baby:
  5 Joules per instruction
ARM968:
  0.000 000 000 1 Joules per instruction
  50,000,000,000 times better than Baby!
(James Prescott Joule born Salford, 1818)
Notes: We can some idea of the relative efficiencies of these two machines by comparing their “fuel efficiency”. In the case of a computer, this is the energy taken to execute one instructions.
Baby consumed about 5 Joules per instruction;
DRACO consumes a whole lot less, namely 100pJ
The ratio of these two numbers is over 2 billion (in fact, 50 billion), which is one of these numbers that comes up in computing technology that is very hard to get a feel for.
If cars had improved by a similar ratio in their fuel efficiency, a few gallons of petrol would be enough to keep the UK mobile for a year, and the oil crisis would be forgotten.
However, there are, of course, good reasons why cars cannot achieve such levels of fuel efficiency. Whereas there is no lower limit to the fuel efficiency of computing – it can, at least in theory, be done with no energy at all…

## Slide 23: 10 more years of progress
Baby, 1948:
  filled a medium-sized room
  used 3.5 kW of electrical power
  executed 700 instructions per second
ARM968, 2005
  fills 0.4mm2 of silicon (130nm)
  uses 20 mW of electrical power
  executes 200,000,000 instructions per second
ARM Cortex-A35, 2015
  smallest area configuration <0.25mm2
  uses less than 4 mW of electrical power at 100 MHz
  executes ~210,000,000 instructions per second
Notes: The ARM® Cortex-A35 processor is ARM’s most power-efficient application processor capable of seamlessly supporting 32-bit and 64-bit compute.
A35 also has a rather larger instruction set to implement, too...
For ARM Cortex-A35, ARM marketing states:
Smallest area configuration 0.25 mm2
Less than 4 mW at 100 MHz
Then, from https://en.wikipedia.org/wiki/Comparison_of_ARMv8-A_cores you can see DMIPS/MHz for A35 = 2.1

## Slide 24: Hardware Design
Power management largely in domain of Hardware Design
  Considerations to minimize/optimize
    Dynamic (switching) and static (leakage) power
  On-chip power management
    Modes: on, standby, suspend, sleep, off
Development of low power electronics
Where can the greatest savings be made?

## Slide 25: Greater Savings at Higher Levels

## Slide 26
ElectronicsWeekly 15-21 June 2011 | No. 2472
Notes: This is a very YOUNG field! Luca tracked research on energy back over the centuries, this field is at best a few years old.

## Slide 27: Wasted Potential
Huge advances have been made in power-efficient hardware.
BUT – potential energy savings are wasted by
  software that does not exploit energy-saving features of hardware;
  poor dynamic management of tasks and resources.

## Slide 28: Energy Efficiency of ICT
soFtware
alGorithms
gAtes
Blocks
arChitecture
Drivers
compilErs
http://www.clker.com/cliparts/f/0/5/1/12937499341853355695circuit-board.jpg
http://static.datixinc.com/wp-content/uploads/2015/04/7.jpg
Notes: Software does not do a good job.
Potential energy savings enabled by low power hardware are wasted by software that does not exploit these.

## Slide 29: The Focus is on Software
Software controls the behaviour of the hardware
  Algorithms and Data Flow
  Compiler (optimizations)
    Traditional SW design goals:
    performance,
    performance,
    performance

## Slide 30: The Focus is on Software
Software engineers often “blissfully unaware”
  Implications of algorithm/code/data on power/energy?
  Power/Energy considerations
    at best, secondary design goals
BUT the biggest savings can be gained from optimizations at the higher levels of abstraction in the system stack
  Algorithms,
  Data and
  SW

## Slide 31
Notes: We need to acknowledge that ultimately, it is the software that controls what the hardware does.

## Slide 32: Aligning SW Design Decisions with Energy Efficiency as Design Goal
“Choose the best algorithm for the problem at hand and make sure it fits well with the computational hardware. Failure to do this can lead to costs far exceeding the benefit of more localized power optimizations.
Minimize memory size and expensive memory accesses through algorithm transformations, efficient mapping of data into memory, and optimal use of memory bandwidth, registers and cache.
Optimize the performance of the application, making maximum use of available parallelism.
Take advantage of hardware support for power management.
Finally, select instructions, sequence them, and order operations in a way that minimizes switching in the CPU and datapath.”
  Kaushik Roy and Mark C. Johnson. 1997. “Software design for low power”. In Low power design in deep submicron electronics, Wolfgang Nebel and Jean Mermet (Eds.). Kluwer Nato Advanced Science Institutes Series, Vol. 337. Kluwer Academic Publishers, Norwell, MA, USA, pp 433-460.
Key steps*:
Notes: Which SW developer tries to match algorithms to hardware?
For decades – moved SW away from HW – productivity, portability, …

## Slide 33: How much?
Picture from www.pd4pic.com
Notes: The problem is:
What we can’t see, we can’t optimize.

## Slide 34: Energy Transparency
http://scottebales.com/wp-content/uploads/2013/05/transparecny-green.jpg
Notes: Information on energy usage is available for programs:
  ideally without executing them, and
  at all levels of abstraction.

## Slide 35: Energy Transparency
Information on energy usage is available for programs:
  ideally without executing them, and
  at all levels from machine code to high-level application code.
35

## Slide 36: Transparency

## Slide 37: Transparency

## Slide 38: Transparency
Notes: We need energy consumption functions, rather than single values. 

## Slide 39: Why Energy Transparency?
Energy transparency enables a deeper understanding of how algorithms and coding impact on the energy consumption of a computation when executed on hardware.
39
Notes: In a nutshell, we can’t improve what we can’t measure! 

## Slide 40: Learning Objectives
Why software is key to energy efficient computing
What energy transparency means and why we need energy transparency to achieve energy efficient computing
How to measure the energy consumed by software
How to estimate the energy consumed by software without measuring
How to construct energy consumption models

## Slide 41: Learning Objectives
Why software is key to energy efficient computing
What energy transparency means and why we need energy transparency to achieve energy efficient computing
How to measure the energy consumed by software
How to estimate the energy consumed by software without measuring
How to construct energy consumption models

## Slide 42: Measuring the Energy Consumption of Computation
Notes: The first step towards energy transparency is being able to *measure*.

## Slide 43: Measuring Power
Measure voltage drop
across the resistor
I = Vshunt / Rshunt to find the current.
Measure voltage at
one side of the resistor
P = I × V to calculate the power.
Notes: Circuitry behind measuring power, how it works

## Slide 44: The Power Monitor
Amplifier
ADC

## Slide 45: Measuring Power
Measure voltage drop
across the resistor
I = Vshunt / Rshunt to find the current
Measure voltage at
one side of the resistor
P = I × V to calculate the power
Repeat frequently, timestamp
each sample
Notes: Circuitry behind measuring power, how it works

## Slide 46: Measuring Energy
Time
Power
Energy
Notes: Power trace
Integrate this - energy

## Slide 47: How much data?
Currently 500,000 Samples/second
6,000,000 S/s possible in bursts
Notes: Stream back over usb, not fast enough
Burst up to 6.000.000
Visualise power traces in gtkwave

## Slide 48: The Showstopper 
Notes: But, soldering is still not part of our CS programmes, nor of any SW Engineering courses. 

## Slide 49: Open Energy Measurement Board
http://mageec.org/
Notes: To bridge this gap…open source, design can be downloaded from mageec.org!

## Slide 50: Open Energy Measurement Board
http://mageec.org/
Notes: To bridge this gap…open source, design can be downloaded from mageec.org!

## Slide 51: Open Energy Measurement Board
http://groundelectronics.com/products/mageec-energy-measurement-kit

## Slide 52: Energy Measurement A hands-on session by Steve Kerrison

## Slide 53: Summary: Energy Measurement
We can directly measure the energy consumed during the execution of a program.
In most cases, specialized hardware and modifications to hardware are required to enable measurement.
The accuracy of the measurements depends on the sampling frequency, on the measuring hardware and on the characteristics of the target you want to measure.

## Slide 54
BREAK
(with the next two slides serving as screen cover during the break)

## Slide 56
56
If you want an ultimate low-power system, then you have to worry about energy usage at every level in the system design, and you have to get it right from top to bottom, because any level at which you get it wrong is going to lose you perhaps an order of magnitude in terms of power efficiency.
The hardware technology has a first-order impact on the power efficiency of the system, but you've also got to have software at the top that avoids waste wherever it can. You need to avoid, for instance, anything that resembles a polling loop because that's just burning power to do nothing.
I think one of the hard questions is whether you can pass the responsibility for the software efficiency right back to the programmer.
Do programmers really have any understanding of how much energy their algorithms consume?
I work in a computer science department, and it's not clear to me that we teach the students much about how long their algorithms take to execute, let alone how much energy they consume in the course of executing and how you go about optimizing an algorithm for its energy consumption.
Some of the responsibility for that will probably get pushed down into compilers, but I still think that fundamentally, at the top level, programmers will not be able to afford to be ignorant about the energy cost of the programs they write.
What you need in order to be able to work in this way at all is instrumentation that tells you that running this algorithm has this kind of energy cost and running that algorithm has that kind of energy cost.
You need tools that give you feedback and tell you how good your decisions are. Currently the tools don't give you that kind of feedback.
February 2010, acmqueue Interview with Steve Furber
The designer of the ARM chip shares lessons on energy-efficient computing at: http://queue.acm.org/detail.cfm?id=1716385
Steve Furber
Notes: acmqueue> We've focused a lot on the hardware, and I think that's a very important
context in the framework of what's going on with energy and computing. Looking
forward, is most of this pursuit to be energy efficient going to be achieved by
advances in the component and hardware technology, or is it also going to have
great consequence for software developers?
56

## Slide 57: Dynamic Energy Monitoring for desktop applications

## Slide 58: The EACOF
A simple Energy-Aware
COmputing Framework
https://github.com/eacof

## Slide 59: High Level
Energy Data From Hardware or OS
EACOF
Application
Provider Central Authority Consumer

## Slide 60: Providers
HDD Provider
EACOF
Application
Battery Provider
CPU Provider
Provider Central Authority Consumer

## Slide 61: Consumers
HDD Provider
EACOF
Battery Provider
CPU Provider
Web Browser
Video Player
Email Client
Provider Central Authority Consumer

## Slide 62: One Machine
HDD Provider
EACOF
Battery Provider
CPU Provider
Web Browser
Video Player
Email Client
Provider Central Authority Consumer

## Slide 63: Networked
HDD Provider
EACOF
Battery Provider
CPU Provider
Web Browser
Video Player
Email Client
HDD Provider
EACOF
Battery Provider
CPU Provider
Web Browser
Video Player
Email Client
HDD Provider
EACOF
Battery Provider
CPU Provider
Web Browser
Video Player
Email Client
HDD Provider
EACOF
Battery Provider
CPU Provider
Web Browser
Video Player
Email Client
Network Analytics

## Slide 64: How to use EACOF

## Slide 65: Simple Provider Example
while(1) {
collectEnergyData();
waitABit();
}

## Slide 66: Simple Provider Example + EACOF
#include <eacof.h>
eacof_Probe *probe;
eacof_Sample sample;
initEACOF();
createProbe(&probe, 1, EACOF_DEVICE_BATTERY_ALL);
while(1) {
sample = collectEnergyData();
addSample(probe, sample);
waitABit();
}
deleteProbe(&probe);

## Slide 67: Simple Consumer Example
for (int i = 0; i < 10000; i++) {
printf(“Hello EACOF!”);
}

## Slide 68: Simple Consumer Example + EACOF
#include <eacof.h>
eacof_Checkpoint *checkpoint;
eacof_Sample sample;
initEACOF();
setCheckpoint(&checkpoint, EACOF_PSPEC_ALL, 1, EACOF_DEVICE_BATTERY_ALL);
for (int i = 0; i < 10000; i++) {
printf(“Hello EACOF!\n”);
sampleCheckpoint(checkpoint, &sample);
}
deleteCheckpoint(&checkpoint);

## Slide 69: The EACOF API
#include <eacof.h>
initEACOF();
createProbe(); deleteProbe();
activateProbe(); deactivateProbe();
addSample();
setCheckpoint(); deleteCheckpoint();
sampleCheckpoint();

## Slide 70: Comparing Sorting Algorithms
Insertion Sort: 32 bit version more optimized
Counting Sort:
75% more energy for 64 bit compared to 8 bit values
Sorting 64 bit values takes less time than sorting 8 bit values, but consumed more energy
Average power variations between algorithms
Sorting of integers in [0,255]
70
H. Field, G. Anderson and K. Eder. “EACOF: A Framework for Providing Energy Transparency to enable Energy-Aware Software Development”. 29th ACM Symposium On Applied Computing. pp. 1194–1199. March 2014, ACM.

## Slide 71: Invitation: EACOF is open source!
github.com/eacof

## Slide 72: Learning Objectives
Why software is key to energy efficient computing
What energy transparency means and why we need energy transparency to achieve energy efficient computing
How to measure the energy consumed by software
How to estimate the energy consumed by software without measuring
How to construct energy consumption models

## Slide 73: Learning Objectives
Why software is key to energy efficient computing
What energy transparency means and why we need energy transparency to achieve energy efficient computing
How to measure the energy consumed by software
How to estimate the energy consumed by software without measuring
How to construct energy consumption models

## Slide 74: Static Analysis of Energy Consumption

## Slide 76: The ENTRA Project
76
Whole Systems ENergy TRAnsparency
EC FP7 FET MINECC:
  “Software models and programming methodologies supporting the strive for the energetic limit
  (e.g. energy cost awareness or exploiting the trade-off between energy and performance/precision).”

## Slide 77: Acknowledgements
The partners in the EU ENTRA project
Steve Kerrison, Kyriakos Gerogiou, James Pallister, Jeremy Morse and Neville Grech
Pedro López García and team
Henk Muller and team
John Gallagher and team

## Slide 78
Static Energy Usage Analysis
int fact (int x) {
if (x<=0)a
return 1b;
return (x *d fact(x-1))c;
}
Cfact(x) = Ca + Cb if x<=0
Cfact(x) = Ca + Cc(x) if x>0
Cc(x) = Cd + Cfact(x-1)
Substitute Ca, Cb, Cd with
the actual energy required to execute the corresponding lower-level (machine) instructions.
Original Program:
Extracted Cost Relations:

## Slide 79: Energy Modelling captures energy consumption

## Slide 80: Modelling Considerations
At what level should we model?
  instruction level, i.e. machine code
  intermediate representation of compiler
  source code
Models require measurements
  need to associate entities at a given level with costs, i.e. energy consumption
    accuracy
    usefulness
Notes: What makes it difficult to associate costs with entities?
how accurate can we associate costs with entities – from source to executable is a long way and the compiler transforms/optimizes the program beyond recognition
How useful is the model:
at ISA
at LLVM IR
at source code -> most useful for software developer

## Slide 81: Modelling Considerations
At what level should we model?
  instruction level, i.e. machine code
  intermediate representation of compiler
  source code
Models require measurements
  need to associate entities at a given level with costs, i.e. energy consumption
    accuracy – the lower the better
    usefulness – the higher the better
http://www.speechinaction.org/wp-content/uploads/2012/10/dilemma.jpg
Notes: What makes it difficult to associate costs with entities?
how accurate can we associate costs with entities – from source to executable is a long way and the compiler transforms/optimizes the program beyond recognition
How useful is the model:
at ISA
at LLVM IR
at source code -> most useful for software developer

## Slide 82: ISA-Level Energy Modelling
Instruction Base Cost, Bi, of each instruction i
Energy Cost (E) of a program (P):
Circuit State Overhead, Oi,j, for each instruction pair
Based on V. Tiwari, S. Malik and A. Wolfe. “Instruction Level Power Analysis and Optimization of Software”, Journal of VLSI Signal Processing Systems, 13, pp 223-238, 1996.
82

## Slide 83: ISA-Level Energy Modelling
Based on V. Tiwari, S. Malik and A. Wolfe. “Instruction Level Power Analysis and Optimization of Software”, Journal of VLSI Signal Processing Systems, 13, pp 223-238, 1996.
83
Components of an Energy Model:
Bi and Oi,j are energy costs.
Characterization of a model through measurement produces these values for a given processor.
Notes: Short excurse into how this may be possible to do:
large loops of each instruction to determine the base costs
large loops of pairs of instructions to determine the switching costs
regression for instructions that can’t easily be tested
Which data should we use?

## Slide 84: ISA-Level Energy Modelling
Based on V. Tiwari, S. Malik and A. Wolfe. “Instruction Level Power Analysis and Optimization of Software”, Journal of VLSI Signal Processing Systems, 13, pp 223-238, 1996.
84
Components of an Energy Model:
Ni is the number of times that instruction i is executed, and
Ni,j is the number of times that the execution of instruction i is followed by the execution of instruction j.
Notes: LATER: How can we obtain these: execution trace, simulation trace, static analysis

## Slide 85: Exercise: E(fact(3))?
int fact (int x) {
int ret = x;
while (--x)
{
ret *= x;
}
return ret;
}
How much energy does a call to fact(3) consume?
fact:
sub r3, r0, #1
cmp r3, #0
beq .L2
.L3:
mul r0, r3
sub r3, r3, #1
cmp r3, #0
bne .L3
.L2:
bx lr
Notes: translate into machine instructions
characterize the energy consumption of instructions – ISA level model

## Slide 86: Base Cost Characterization
Instruction | Base Cost [pJ]
sub | 600
cmp | 300
beq | 500
mul | 900
bne | 500
bx | 700
fact:
sub r3, r0, #1
cmp r3, #0
beq .L2
.L3:
mul r0, r3
sub r3, r3, #1
cmp r3, #0
bne .L3
.L2:
bx lr
Notes: If we take the values for B and O to be in pJ, and imagine the processor runs at 100 MHz, then the base power of beq would be 500 pJ / 10 ns, which is 50 mW, which is a sensible value (anything from 1 mW to 100 mW is probably OK, depending on the processor imagined). The overheads are small to about the proportion we see on an XCore (10%) so again are sensible.

## Slide 87: Overhead Characterization
Oi,j [pJ] | beq | bne | bx | cmp | mul | sub
beq | 0 | 10 | 10 | 30 | 30 | 30
bne | 10 | 0 | 10 | 30 | 30 | 30
bx | 10 | 10 | 0 | 60 | 60 | 60
cmp | 10 | 10 | 10 | 0 | 20 | 20
mul | 10 | 10 | 10 | 30 | 0 | 30
sub | 10 | 10 | 10 | 20 | 30 | 0
fact:
sub r3, r0, #1
cmp r3, #0
beq .L2
.L3:
mul r0, r3
sub r3, r3, #1
cmp r3, #0
bne .L3
.L2:
bx lr
Notes: If we take the values for B and O to be in pJ, and imagine the processor runs at 100 MHz, then the base power of beq would be 500 pJ / 10 ns, which is 50 mW, which is a sensible value (anything from 1 mW to 100 mW is probably OK, depending on the processor imagined). The overheads are small to about the proportion we see on an XCore (10%) so again are sensible.

## Slide 88: Instruction Characterization
Instruction | Base Cost [pJ]
beq | 500
bne | 500
bx | 700
cmp | 300
mul | 900
sub | 600
Oi,j [pJ] | beq | bne | bx | cmp | mul | sub
beq | 0 | 10 | 10 | 30 | 30 | 30
bne | 10 | 0 | 10 | 30 | 30 | 30
bx | 10 | 10 | 0 | 60 | 60 | 60
cmp | 10 | 10 | 10 | 0 | 20 | 20
mul | 10 | 10 | 10 | 30 | 0 | 30
sub | 10 | 10 | 10 | 20 | 30 | 0
Notes: If we take the values for B and O to be in pJ, and imagine the processor runs at 100 MHz, then the base power of beq would be 500 pJ / 10 ns, which is 50 mW, which is a sensible value (anything from 1 mW to 100 mW is probably OK, depending on the processor imagined). The overheads are small to about the proportion we see on an XCore (10%) so again are sensible.

## Slide 89: ISA-Level Energy Modelling
Based on V. Tiwari, S. Malik and A. Wolfe. “Instruction Level Power Analysis and Optimization of Software”, Journal of VLSI Signal Processing Systems, 13, pp 223-238, 1996.
89
Components of an Energy Model:
Instruction | Base Cost [pJ]
beq | 500
bne | 500
bx | 700
cmp | 300
mul | 900
sub | 600
Oi,j [pJ] | beq | bne | bx | cmp | mul | sub
beq | 0 | 10 | 10 | 30 | 30 | 30
bne | 10 | 0 | 10 | 30 | 30 | 30
bx | 10 | 10 | 0 | 60 | 60 | 60
cmp | 10 | 10 | 10 | 0 | 20 | 20
mul | 10 | 10 | 10 | 30 | 0 | 30
sub | 10 | 10 | 10 | 20 | 30 | 0
Notes: Short excurse into how this may be possible to do:
large loops of each instruction to determine the base costs
large loops of pairs of instructions to determine the switching costs
regression for instructions that can’t easily be tested
Which data should we use?

## Slide 90: ISA-Level Energy Modelling
V. Tiwari, S. Malik and A. Wolfe. “Instruction Level Power Analysis and Optimization of Software”, Journal of VLSI Signal Processing Systems, 13, pp 223-238, 1996.
90
Components of an Energy Model:
Ni and Ni,j represent the number of times specific instructions and instruction pairs are executed.
How can we determine these?
Notes: Focus here on “executing” the program by hand, then go into simulation (speed is a concern), then static analysis.
Simulation is typically orders of magnitude slower than running the program.

## Slide 91: Exercise
@ Argument is in r0
fact:
sub r3, r0, #1
cmp r3, #0
beq .L2 @ Never iterate loop if num == 1
.L3:
mul r0, r3 @ Accumulate factorial value in r0
sub r3, r3, #1 @ r3 is decrementing counter
cmp r3, #0
bne .L3 @ Loop if we haven't reached 0
.L2:
bx lr @ Return, answer is in r0
Which instruction sequence is being executed for a call to fact(3)?
Notes: determine trace of instructions to be executed to calculate fact(3), fact(3) = 1*2*3=6
this would be: sub, cmp, beq (not taken), mul, sub, cmp,

## Slide 92: Exercise
@ Argument is in r0
fact:
sub r3, r0, #1
cmp r3, #0
beq .L2 @ Never iterate loop if num == 1
.L3:
mul r0, r3 @ Accumulate factorial value in r0
sub r3, r3, #1 @ r3 is decrementing counter
cmp r3, #0
bne .L3 @ Loop if we haven't reached 0
.L2:
bx lr @ Return, answer is in r0
A call to fact(3) would invoke the following instructions in this order:
sub, cmp, beq (not taken),
mul, sub, cmp, bne (taken),
mul, sub, cmp, bne (not taken),
bx
Notes: determine trace of instructions to be executed to calculate fact(3), fact(3) = 1*2*3=6
this would be: sub, cmp, beq (not taken), mul, sub, cmp,

## Slide 93: Exercise
Instruction | Base Cost [pJ]
beq | 500
bne | 500
bx | 700
cmp | 300
mul | 900
sub | 600
Oi,j [pJ] | beq | bne | bx | cmp | mul | sub
beq | 0 | 10 | 10 | 30 | 30 | 30
bne | 10 | 0 | 10 | 30 | 30 | 30
bx | 10 | 10 | 0 | 60 | 60 | 60
cmp | 10 | 10 | 10 | 0 | 20 | 20
mul | 10 | 10 | 10 | 30 | 0 | 30
sub | 10 | 10 | 10 | 20 | 30 | 0
A call to fact(3) would invoke the following instructions in this order:
sub, cmp, beq (not taken),
mul, sub, cmp, bne (taken),
mul, sub, cmp, bne (not taken),
bx
Notes: determine trace of instructions to be executed to calculate fact(3), fact(3) = 1*2*3=6
this would be: sub, cmp, beq (not taken), mul, sub, cmp,

## Slide 94: Exercise
sub, cmp, beq (not taken), mul, sub, cmp, bne (taken), mul, sub, cmp, bne (not taken), bx
Efact(3) =
Notes: determine trace of instructions to be executed to calculate fact(3), fact(3) = 1*2*3=6
this would be: sub, cmp, beq (not taken), mul, sub, cmp,

## Slide 95: Exercise
sub, cmp, beq (not taken), mul, sub, cmp, bne (taken), mul, sub, cmp, bne (not taken), bx
Efact(3) = 3*600pJ + 3*300pJ + 500pJ +2*900 + 2*500pJ + 700pJ
+ 3*20pJ + 10pJ + 30pJ + 2*30pJ + 2*10pJ + 30pJ + 10pJ
= 6920pJ = 6.92nJ
Notes: determine trace of instructions to be executed to calculate fact(3), fact(3) = 1*2*3=6
this would be: sub, cmp, beq (not taken), mul, sub, cmp, bne (taken), mul, sub, cmp, bne (not taken), bx
then use the equation to determine the energy cost of a call to fact(3)
But, is it really this simple? Discussion of E_P formula leading to E_k instruction effects from u-arch!

## Slide 96: Is it really this easy?
Instruction Base Cost, Bi, of each instruction i
Energy Cost (E) of a program (P):
Circuit State Overhead, Oi,j, for each instruction pair
Based on V. Tiwari, S. Malik and A. Wolfe. “Instruction Level Power Analysis and Optimization of Software”, Journal of VLSI Signal Processing Systems, 13, pp 223-238, 1996.
96
Notes: Is it really this easy?
E_k is processor specific: u-architecture – pipelining, caches, etc.
This is hard to predict based on the source code alone – impossible in practice!

## Slide 97: Is it really this easy?
Instruction Base Cost, Bi, of each instruction i
Energy Cost (E) of a program (P):
Circuit State Overhead, Oi,j, for each instruction pair
V. Tiwari, S. Malik and A. Wolfe. “Instruction Level Power Analysis and Optimization of Software”, Journal of VLSI Signal Processing Systems, 13, pp 223-238, 1996.
Other Instruction Effects
97
Notes: Is it really this easy?
E_k is processor specific: u-architecture – pipelining, caches, etc.
This is hard to predict based on the source code alone – impossible in practice!

## Slide 98: Energy Modelling
Instruction Base Cost, Bi, of each instruction i
Energy Cost (E) of a program (P):
Circuit State Overhead, Oi,j, for each instruction pair
V. Tiwari, S. Malik and A. Wolfe. “Instruction Level Power Analysis and Optimization of Software”, Journal of VLSI Signal Processing Systems, 13, pp 223-238, 1996.
Other Instruction Effects (stalls, cache misses, etc)
98
Notes: E_k is processor specific: u-architecture – pipelining, caches, etc.
Each E_k = C_Ek * N_Ek
These are very hard to predict based on the source code alone – often impossible in practice!

## Slide 99
XCore Energy Modelling
Concurrency cost, instruction cost, generalised overhead, base power and duration
Energy Cost (E) of a multi-threaded program (P):
Use of execution statistics rather than execution trace.
Fast running model with an average error margin of less than 7%.
Idle base power and duration
S. Kerrison and K. Eder. 2015. “Energy Modeling of Software for a Hardware Multithreaded Embedded Microprocessor”. ACM Trans. Embed. Comput. Syst. 14, 3, Article 56 (April 2015), 25 pages. DOI=10.1145/2700104 http://doi.acm.org/10.1145/2700104

## Slide 100: The set up...
S. Kerrison and K. Eder. 2015. “Energy Modeling of Software for a Hardware Multithreaded Embedded Microprocessor”. ACM Trans. Embed. Comput. Syst. 14, 3, Article 56 (April 2015), 25 pages. DOI=10.1145/2700104 http://doi.acm.org/10.1145/2700104

## Slide 101
ISA Characterization

## Slide 102
ISA Characterization
S. Kerrison and K. Eder. 2015. “Energy Modeling of Software for a Hardware Multithreaded Embedded Microprocessor”. ACM Trans. Embed. Comput. Syst. 14, 3, Article 56 (April 2015), 25 pages. DOI=10.1145/2700104 http://doi.acm.org/10.1145/2700104
Notes: Focus on data, here data width – but what about the impact of data in general?

## Slide 103: a*b = b*a
Notes: We all know that a*b=b*a, but did you know that E(a*b) != E(b*a)
I've attached the mul graph.
Details about the AVR mul:
16 bit result, (implicitly) stored in r1:r0
mul X, Y (x-axis of the graph is the first operand)
Colour bar units: joules

## Slide 104: Energy(a*b) ≠ Energy(b*a)

## Slide 105
ISA Characterization
Notes: ISA level models often associate a single cost with each instruction – this represents the average of the measurements obtained over multiple runs using randomly generated valid data.
Is this correct?
What data should we use?
use case data – use case is not known at the time when the energy model is being built
random data – empirical evaluation suggests that this is close to the WC [Tiwari did this and so did we.]

## Slide 106: The Impact of Data on Energy Consumption
Notes: What happens here? The previous picture was assigning a single energy cost to each instruction – averaged over randomly generated valid data.
Here, we see an exhaustive map for “SUB” for all 8 bit values. Why blue/red? (2’s complement for negative results gives lots of leading ones, so lots of switching!)

## Slide 107: W/A/B-Case Energy Consumption
Notes: These show the overhead caused by different data, i.e. on top of the instruction base cost.
Note, the colour scale is not the same for each!!!

## Slide 108: A quick jump forward to Static Resource consumption Analysis

## Slide 109: Static Resource Analysis
109
Techniques automatically infer upper and lower bounds on resource usage of a program.
Bounds expressed using monotonic arithmetic functions per procedure parameterized by program’s input size.
Verification can be done statically by checking that the upper and lower bounds on resource usage defined in the specifications hold.
Notes: Static cost analysis techniques based on setting up and solving recurrence equations date back to Wegbreit’s seminal work in 1975,
and have been developed significantly in subsequent work.

## Slide 110: Specified Resource Usage
Source: Pedro Lopez Garcia, IMDEA Software Research Institute
110

## Slide 111: Analysis Result
Source: Pedro Lopez Garcia, IMDEA Software Research Institute
111

## Slide 112: Verification
Source: Pedro Lopez Garcia, IMDEA Software Research Institute
112

## Slide 113: Worst Case Execution Time
Worst Case Execution Time (WCET) Analysis:
  WCET model
  WCET bounds (are often safety critical)
    safe, i.e. no underestimation
    tight, i.e. ideally very little overestimation
Does this work for energy consumption analysis?
From “The Worst-Case Execution-Time Problem — Overview of Methods and Survey of Tools” by WILHELM et al. (2008)
Notes: For example, let’s look at WCETime Analysis – area that has attracted research interest for decades.
WCET bounds could be safety critical!

## Slide 114: Worst Case Energy Consumption
WCEC analysis goes well beyond WCET analysis.
  data independence of execution time through the use of synchronous logic
  embedded real-time systems that are timing predictable execute instructions in a fixed number of clock cycles
  WCET then depends only on the WC execution path
Energy consumption is data dependent.
  Data dependent energy modelling
Notes: The worst case energy consumption problem goes beyond the worst case execution time problem,
because the execution time of a single instruction is largely independent of its input data. This is
because timing variability has mostly been eliminated “by design" through the use of synchronous
logic and the limited propagation time associated with executing individual instructions.
In real-time embedded systems, timing-predictable processors execute instructions within a
fixed number of clock cycles, irrespective of the data the operation works on. This is particularly
beneficial to WCET analysis, which can then focus on identifying the worst case execution
path which is determined by the control flow, rather than by the data flow of the computation.

## Slide 116: Worst Case Energy Consumption
WCEC analysis goes well beyond WCET analysis.
  data independence of execution time through the use of synchronous logic
  embedded real-time systems that are timing predictable execute instructions in a fixed number of clock cycles
  WCET then depends only on the WC execution path
Energy consumption is data dependent.
  Data dependent energy modelling
  Critical questions:
    Which data should be used to characterize a WCEC model?
    Which data causes the WCEC for a given program?
    Which data triggers the most switching during the execution of the program?
Notes: The worst case energy consumption problem goes beyond the worst case execution time problem,
because the execution time of a single instruction is largely independent of its input data. This is
because timing variability has mostly been eliminated “by design" through the use of synchronous
logic and the limited propagation time associated with executing individual instructions.
In real-time embedded systems, timing-predictable processors execute instructions within a
fixed number of clock cycles, irrespective of the data the operation works on. This is particularly
beneficial to WCET analysis, which can then focus on identifying the worst case execution
path which is determined by the control flow, rather than by the data flow of the computation.

## Slide 118: Impact of datapath switching
J. Morse, S. Kerrison and K. Eder. 2016. “On the infeasibility of analysing worst case dynamic energy”. (under review) http://arxiv.org/abs/1603.02580
Notes: - Dynamic Power of add instruction in mW
Hamming weight of output datapath in number of bits set
Dynamic power in mW for add instruction, with output datapath cost subtracted (assuming 4.4mW per bit)
Hamming weight of both input operands to an add instruction, in number of bits set
Dynamic power in mW with input datapath cost subtracted (assuming 1.3mW per bit)
Dynamic power in mW with output and input datapath costs subtracted
The Hamming weight of a string is the number of symbols that are different from the zero-symbol of the alphabet used. It is thus equivalent to the Hamming distance from the all-zero string of the same length. For the most typical case, a string of bits, this is the number of 1's in the string.

## Slide 119: Energy Consumption Analysis enables energy transparency
www.theguardian.com

## Slide 120
http://us.123rf.com/450wm/kentoh/kentoh1006/kentoh100600301/7129999-futuristic-technology-data-flow-as-art-background.jpg
www.theguardian.com
Energy Consumption Analysis enables energy transparency

## Slide 121: SRA at the ISA Level
Combine static resource analysis (SRA) with the ISA-level energy model.
Provide energy consumption function parameterised by some property of the program or its data.

## Slide 122
Static Energy Usage Analysis
int fact (int x) {
if (x<=0)a
return 1b;
return (x *d fact(x-1))c;
}
Cfact(x) = Ca + Cb if x<=0
Cfact(x) = Ca + Cc(x) if x>0
Cc(x) = Cd + Cfact(x-1)
Substitute Ca, Cb, Cd with
the actual energy required to execute the corresponding lower-level (machine) instructions.
Solve equation using off-the-shelf solvers.
Result: Cfact(x) = (26x + 19.4) nJ
  (Note: The above result is based on the XMOS XCore Energy model
  introduced earlier. It is not using the energy model from the Exercise.)
Original Program:
Extracted Cost Relations:
122

## Slide 123: ISA-Level Analysis Results
U. Liqat, S. Kerrison, A. Serrano, K. Georgiou, N. Grech, P. Lopez-Garcia, M.V. Hermenegildo and K. Eder. “Energy Consumption Analysis of Programs based on XMOS ISA-Level Models”. LOPSTR 2013.

## Slide 124: ISA-Level Analysis Results
U. Liqat, S. Kerrison, A. Serrano, K. Georgiou, N. Grech, P. Lopez-Garcia, M.V. Hermenegildo and K. Eder. “Energy Consumption Analysis of Programs based on XMOS ISA-Level Models”. LOPSTR 2013.

## Slide 125: Analysis Options
125
Moving away from the underlying model risks loss of accuracy.
But it brings us closer to the original source code.
Notes: A larger class of programs can be analyzed at LLVM IR level than at ISA level, because the LLVM IR level retains a lot of information on code structure and typing, which is lost at the ISA level.

## Slide 126: Energy Consumption of LLVM IR
U. Liqat, K. Georgiou, S. Kerrison, P. Lopez-Garcia, J.P. Gallagher, M.V. Hermenegildo, K. Eder. Inferring Parametric Energy Consumption Functions at Different Software Levels: ISA vs. LLVM IR. In Proceedings of FOPARA 2015. http://arxiv.org/abs/1511.01413
K. Georgiou, S. Kerrison and K. Eder, Oct 2015. “On the Value and Limits of Multi-level Energy Consumption Static Analysis for Deeply Embedded Single and Multi-threaded Programs”. http://arxiv.org/abs/1510.07095

## Slide 127: Analysis at the LLVM-IR Level
N. Grech, K. Georgiou, J. Pallister, S. Kerrison, J. Morse, K. Eder. 2015. Static analysis of energy consumption for LLVM IR programs. In Proceedings of the 18th International Workshop on Software and Compilers for Embedded Systems (SCOPES '15). ACM, New York, NY, USA, pages 12-21. http://dx.doi.org/10.1145/2764967.2764974

## Slide 128: Learning Objectives
Why software is key to energy efficient computing
What energy transparency means and why we need energy transparency to achieve energy efficient computing
How to measure the energy consumed by software
How to estimate the energy consumed by software without measuring
How to construct energy consumption models

## Slide 129: Towards Energy Aware Software Engineering

## Slide 130: Energy Transparency
130
For HW designers:
“Power is a 1st and last order design constraint.”
[Dan Hutcheson, VLSI Research, Inc., E3S Keynote 2011]
“Every design is a point in a 2D plane.”
[Mark Horowitz,E3S 2009]

## Slide 131: Energy Transparency
131
For HW designers:
“Power is a 1st and last order design constraint.”
[Dan Hutcheson, VLSI Research, Inc., E3S Keynote 2011]
“Every design is a point in a 2D plane.”
[Mark Horowitz,E3S 2009]

## Slide 132: Energy Transparency
132
For HW designers:
“Power is a 1st and last order design constraint.”
[Dan Hutcheson, VLSI Research, Inc., E3S Keynote 2011]
“Every design is a point in a 2D plane.”
[Mark Horowitz,E3S 2009]

## Slide 133: Energy Transparency
133
For HW designers:
“Power is a 1st and last order design constraint.”
[Dan Hutcheson, VLSI Research, Inc., E3S Keynote 2011]
“Every design is a point in a 2D plane.”
[Mark Horowitz,E3S 2009]

## Slide 134: More POWER to SW Developers
Full Energy Transparency
from HW to SW
Location-centric programming model
134
    in 5pJ do {...}
“Cool” code for green software
A cool programming competition!
Promoting energy efficiency
to a 1st class SW design goal is
still a very important
research challenge.
Pictures taken from the Energy Efficient Computing Brochure at: https://connect.innovateuk.org/documents/3158891/9517074/Energy%20Efficient%20Computing%20Magazine?version=1.0
Notes: For decades, moved SW dev away from HW – need to bridge the gap!
Location-centric programming to expose cost of communication to developers 

## Slide 135
135
If you want an ultimate low-power system, then you have to worry about energy usage at every level in the system design, and you have to get it right from top to bottom, because any level at which you get it wrong is going to lose you perhaps an order of magnitude in terms of power efficiency.
The hardware technology has a first-order impact on the power efficiency of the system, but you've also got to have software at the top that avoids waste wherever it can. You need to avoid, for instance, anything that resembles a polling loop because that's just burning power to do nothing.
I think one of the hard questions is whether you can pass the responsibility for the software efficiency right back to the programmer.
Do programmers really have any understanding of how much energy their algorithms consume?
I work in a computer science department, and it's not clear to me that we teach the students much about how long their algorithms take to execute, let alone how much energy they consume in the course of executing and how you go about optimizing an algorithm for its energy consumption.
Some of the responsibility for that will probably get pushed down into compilers, but I still think that fundamentally, at the top level, programmers will not be able to afford to be ignorant about the energy cost of the programs they write.
What you need in order to be able to work in this way at all is instrumentation that tells you that running this algorithm has this kind of energy cost and running that algorithm has that kind of energy cost.
You need tools that give you feedback and tell you how good your decisions are. Currently the tools don't give you that kind of feedback.
February 2010, acmqueue Interview with Steve Furber
The designer of the ARM chip shares lessons on energy-efficient computing at: http://queue.acm.org/detail.cfm?id=1716385
Steve Furber
Notes: acmqueue> We've focused a lot on the hardware, and I think that's a very important
context in the framework of what's going on with energy and computing. Looking
forward, is most of this pursuit to be energy efficient going to be achieved by
advances in the component and hardware technology, or is it also going to have
great consequence for software developers?
135

## Slide 136
Thank you for your attention
Kerstin.Eder@bristol.ac.uk