## Slide 1
Department of
COMPUTER SCIENCE
Software and
energy aware computing
Kerstin Eder
Design Automation and Verification, Microelectronics
Verification and Validation for Safety in Robots, Bristol Robotics Laboratory

## Slide 2: Bristol

## Slide 3: The University of Bristol
1876, University College
UoB founded in 1909
  The first higher education institution in England to admit women on an equal basis to men. 
Top 30 universities globally
(QS World University Rankings)
6 Faculties
~14.000 students, 2.000 in FEN
Computer Science in FEN
EACO Workshops

## Slide 4
Department of
COMPUTER SCIENCE
Software and
energy aware computing
Kerstin Eder
Design Automation and Verification, Microelectronics
Verification and Validation for Safety in Robots, Bristol Robotics Laboratory
More power to software developers!

## Slide 5: Overview
Introduction and Motivation
  Energy consumption of Computing
  Software vs Hardware

## Slide 6: Overview
Introduction and Motivation
  Energy consumption of Computing
  Software vs Hardware
  Energy Transparency
Measuring the energy consumption of software
  Demonstration with hands-on session by Steve Kerrison
Energy modeling
Fundamentals of static analysis of software
Static analysis and optimization

## Slide 7: Learning Objectives
Why software is key to energy efficient computing
What energy transparency means and why we need energy transparency to achieve energy efficient computing
How to measure the energy consumed by software
How to construct energy consumption models
How to estimate the energy consumed by software without measuring
What holds us back and what is left to do

## Slide 8: Introduction and Motivation
Pictures taken from the Energy Efficient Computing Brochure at: https://connect.innovateuk.org/documents/3158891/9517074/Energy%20Efficient%20Computing%20Magazine?version=1.0
Notes: This calls for Energy Aware System Design

## Slide 9
Pictures taken from the Energy Efficient Computing Brochure at: https://connect.innovateuk.org/documents/3158891/9517074/Energy%20Efficient%20Computing%20Magazine?version=1.0
Notes: Whether embedded systems, mobile devices, or the large-scale systems that help predict the weather

## Slide 10
Pictures taken from the Energy Efficient Computing Brochure at: https://connect.innovateuk.org/documents/3158891/9517074/Energy%20Efficient%20Computing%20Magazine?version=1.0
Notes: Energy efficiency is the limiting factor in system design.
Energy has become the primary limiting factor in the development of all systems, whether due to the cost of energy or cooling in large systems or due to battery life in mobile devices.

## Slide 11: Electricity Consumption (Billion kwH, 2007)
UK
Greenpeace’s Make IT Green Report, 2010.
http://www.greenpeace.org/international/en/publications/Campaign-reports/Climate-Reports/How-Clean-is-Your-Cloud/
UK
Cloud computing
Notes: More than 10% of the world’s energy consumption is spent on computing.
IT creates 50% more CO2 than the aviation sector. (2014)
Cloudland is the 5th largest consumer of electricity – consuming almost twice as much as the UK!
http://www.vertatique.com/ict-10-global-energy-consumption
http://www.vertatique.com/what-attached-our-global-ict-infrastructure

## Slide 12
“Despite improved energy efficiency, energy consumption through electronic devices will triple until 2030 because of a massive rise in overall demand.”
12
Notes: Predictions suggest that energy consumption through electronic devices will TRIPLE until 2030

## Slide 13: Crowds in St. Peter’s Square
http://www.spiegel.de/panorama/bild-889031-473266.html
2005
2013
Notes: In less than 10 years the same scene looks very different.
Since 2014 the number of electronic devices has more than doubled – being estimated at 19 Billion at the moment.
There are officially more mobile devices than people in the world 2014 – 7.2 Billion.
Estimates now 19 Billion.

## Slide 14: Energy Aware Computing
Notes: This calls for Energy Aware System Design

## Slide 15: Energy Efficiency of ICT
gAtes
Blocks
arChitecture
http://www.clker.com/cliparts/f/0/5/1/12937499341853355695circuit-board.jpg
Notes: Low power has been the focus for hardware developers for more than a decade with great success.

## Slide 16: Hardware Design
Power management largely in domain of Hardware Design
  Considerations to minimize/optimize
    Dynamic (switching) and static (leakage) power
  On-chip power management
    Modes: on, standby, suspend, sleep, off
Development of low power electronics
Where can the greatest savings be made?

## Slide 17: Greater Savings at Higher Levels

## Slide 18
ElectronicsWeekly 15-21 June 2011 | No. 2472

## Slide 19: Wasted Potential
Huge advances have been made in power-efficient hardware.
BUT – potential energy savings are wasted by
  software that does not exploit energy-saving features of hardware;
  poor dynamic management of tasks and resources.

## Slide 20: Energy Efficiency of ICT
soFtware
alGorithms
gAtes
Blocks
arChitecture
Drivers
compilErs
http://www.clker.com/cliparts/f/0/5/1/12937499341853355695circuit-board.jpg
http://static.datixinc.com/wp-content/uploads/2015/04/7.jpg
Notes: Software does not do a good job.
Potential energy savings enabled by low power hardware are wasted by software that does not exploit these.

## Slide 21: The Focus is on Software
Software controls the behaviour of the hardware
  Algorithms and Data Flow
  Compiler (optimizations)
    Traditional SW design goals:
    performance,
    performance,
    performance

## Slide 22: The Focus is on Software
Software engineers often “blissfully unaware”
  Implications of algorithm/code/data on power/energy?
  Power/Energy considerations
    at best, secondary design goals
BUT the biggest savings can be gained from optimizations at the higher levels of abstraction in the system stack
  Algorithms,
  Data and
  SW

## Slide 23
Notes: We need to acknowledge that ultimately, it is the software that controls what the hardware does.

## Slide 24: Aligning SW Design Decisions with Energy Efficiency as Design Goal
“Choose the best algorithm for the problem at hand and make sure it fits well with the computational hardware. Failure to do this can lead to costs far exceeding the benefit of more localized power optimizations.
Minimize memory size and expensive memory accesses through algorithm transformations, efficient mapping of data into memory, and optimal use of memory bandwidth, registers and cache.
Optimize the performance of the application, making maximum use of available parallelism.
Take advantage of hardware support for power management.
Finally, select instructions, sequence them, and order operations in a way that minimizes switching in the CPU and datapath.”
  Kaushik Roy and Mark C. Johnson. 1997. “Software design for low power”. In Low power design in deep submicron electronics, Wolfgang Nebel and Jean Mermet (Eds.). Kluwer Nato Advanced Science Institutes Series, Vol. 337. Kluwer Academic Publishers, Norwell, MA, USA, pp 433-460.
Key steps*:
Notes: Which SW developer tries to match algorithms to hardware?
For decades – moved SW away from HW – productivity, portability, …

## Slide 25: Energy Transparency
Notes: Information on energy usage is available for programs:
  ideally without executing them, and
  at all levels of abstraction.

## Slide 26: Energy Transparency
Information on energy usage is available for programs:
  ideally without executing them, and
  at all levels from machine code to high-level application code.
26

## Slide 27: Transparency

## Slide 28: Transparency

## Slide 29: Transparency
Notes: We need energy consumption functions, rather than single values. 

## Slide 30: Why Energy Transparency?
Energy transparency enables a deeper understanding of how algorithms and coding impact on the energy consumption of a computation when executed on hardware.
30
Notes: In a nutshell, we can’t improve what we can’t measure! 

## Slide 31: Measuring the Energy Consumption of Computation
Notes: The first step towards energy transparency is being able to *measure*.

## Slide 32: Measuring Power
Measure voltage drop
across the resistor
I = Vshunt / Rshunt to find the current.
Measure voltage at
one side of the resistor
P = I × V to calculate the power.
Notes: Circuitry behind measuring power, how it works

## Slide 33: The Power Monitor
Amplifier
ADC

## Slide 34: Measuring Power
Measure voltage drop
across the resistor
I = Vshunt / Rshunt to find the current
Measure voltage at
one side of the resistor
P = I × V to calculate the power
Repeat frequently, timestamp
each sample
Notes: Circuitry behind measuring power, how it works

## Slide 35: Measuring Energy
Time
Power
Energy
Notes: Power trace
Integrate this - energy

## Slide 36: How much data?
Currently 500,000 Samples/second
6,000,000 S/s possible in bursts
Notes: Stream back over usb, not fast enough
Burst up to 6000000
Visualise power traces in gtkwave

## Slide 37: The Showstopper 
Notes: But, soldering is still not part of our CS programmes, nor of any SW Engineering courses. 

## Slide 38: Open Energy Measurement Board
http://mageec.org/
Notes: To bridge this gap…open source, design can be downloaded from mageec.org!

## Slide 39: Open Energy Measurement Board
http://mageec.org/
Notes: To bridge this gap…open source, design can be downloaded from mageec.org!

## Slide 40: Open Energy Measurement Board
http://groundelectronics.com/products/mageec-energy-measurement-kit

## Slide 41: Dynamic Energy Monitoring

## Slide 42: The EACOF
A simple Energy-Aware
COmputing Framework
https://github.com/eacof

## Slide 43: High Level
Energy Data From Hardware or OS
EACOF
Application
Provider Central Authority Consumer

## Slide 44: Providers
HDD Provider
EACOF
Application
Battery Provider
CPU Provider
Provider Central Authority Consumer

## Slide 45: Consumers
HDD Provider
EACOF
Battery Provider
CPU Provider
Web Browser
Video Player
Email Client
Provider Central Authority Consumer

## Slide 46: Comparing Sorting Algorithms
Insertion Sort: 32 bit version more optimized
Counting Sort:
75% more energy for 64 bit compared to 8 bit values
Sorting 64 bit values takes less time than sorting 8 bit values, but consumed more energy
Average power variations between algorithms
Sorting of integers in [0,255]
46
H. Field, G. Anderson and K. Eder. “EACOF: A Framework for Providing Energy Transparency to enable Energy-Aware Software Development”. 29th ACM Symposium On Applied Computing. pp. 1194–1199. March 2014, ACM.

## Slide 47: Invitation: EACOF is open source!
github.com/eacof

## Slide 48: Static Analysis for Energy Consumption

## Slide 50: The ENTRA Project
50
Whole Systems ENergy TRAnsparency
EC FP7 FET MINECC:
  “Software models and programming methodologies supporting the strive for the energetic limit
  (e.g. energy cost awareness or exploiting the trade-off between energy and performance/precision).”

## Slide 51: SRA for Energy Consumption
51
Adaptation of traditional resource usage analysis techniques to energy consumption.
Techniques automatically infer upper and lower bounds on energy usage of a program.
Bounds expressed using monotonic arithmetic functions per procedure parameterized by program’s input size.
Verification can be done statically by checking that the upper and lower bounds on energy usage and any other resource defined in the specifications hold.
Notes: Static cost analysis techniques based on setting up and solving recurrence equations date back to Wegbreit’s seminal work in 1975,
and have been developed significantly in subsequent work.

## Slide 52: Specified Resource Usage
Source: Pedro Lopez Garcia, IMDEA Software Research Institute
52

## Slide 53: Analysis Result
Source: Pedro Lopez Garcia, IMDEA Software Research Institute
53

## Slide 54: Verification
Source: Pedro Lopez Garcia, IMDEA Software Research Institute
54

## Slide 55
Static Energy Usage Analysis
int fact (int x) {
if (x<=0)a
return 1b;
return (x *d fact(x-1))c;
}
Cfact(x) = Ca + Cb if x<=0
Cfact(x) = Ca + Cc(x) if x>0
Cc(x) = Cd + Cfact(x-1)
Substitute Ca, Cb, Cd with
the actual energy required to execute the corresponding lower-level (machine) instructions.
Original Program:
Extracted Cost Relations:

## Slide 56: Energy Modelling captures energy consumption

## Slide 57: Energy Modelling
Instruction Base Cost, Bi, of each instruction i
Energy Cost (E) of a program (P):
Circuit State Overhead, Oi,j, for each instruction pair
V. Tiwari, S. Malik and A. Wolfe. “Instruction Level Power Analysis and Optimization of Software”, Journal of VLSI Signal Processing Systems, 13, pp 223-238, 1996.
Other Instruction Effects (stalls, cache misses, etc)
57

## Slide 58
XCore Energy Modelling
Concurrency cost, instruction cost, generalised overhead, base power and duration
Energy Cost (E) of a multi-threaded program (P):
Use of execution statistics rather than execution trace.
Fast running model with an average error margin of less than 7%
Idle base power and duration
S. Kerrison and K. Eder. 2015. “Energy Modeling of Software for a Hardware Multithreaded Embedded Microprocessor”. ACM Trans. Embed. Comput. Syst. 14, 3, Article 56 (April 2015), 25 pages. DOI=10.1145/2700104 http://doi.acm.org/10.1145/2700104

## Slide 59: The set up...
S. Kerrison and K. Eder. 2015. “Energy Modeling of Software for a Hardware Multithreaded Embedded Microprocessor”. ACM Trans. Embed. Comput. Syst. 14, 3, Article 56 (April 2015), 25 pages. DOI=10.1145/2700104 http://doi.acm.org/10.1145/2700104

## Slide 60
ISA Characterization

## Slide 61
ISA Characterization
S. Kerrison and K. Eder. 2015. “Energy Modeling of Software for a Hardware Multithreaded Embedded Microprocessor”. ACM Trans. Embed. Comput. Syst. 14, 3, Article 56 (April 2015), 25 pages. DOI=10.1145/2700104 http://doi.acm.org/10.1145/2700104

## Slide 62: a*b = b*a
Notes: We all know that a*b=b*a, but did you know that E(a*b != E(b*a)
I've attached the mul graph.
Details about the AVR mul:
16 bit result, (implicitly) stored in r1:r0
mul X, Y (x-axis of the graph is the first operand)
Colour bar units: joules

## Slide 63: Energy(a*b) ≠ Energy(b*a)

## Slide 64
ISA Characterization

## Slide 65: W/A/B-Case Energy Consumption

## Slide 66: W/A/B-Case Energy Consumption
Notes: These show the overhead caused by different data, i.e. on top of the instruction base cost.
Note, the colour scale is not the same for each!!!

## Slide 69: Impact of datapath switching
J. Morse, S. Kerrison and K. Eder. 2016. “On the infeasibility of analysing worst case dynamic energy”. (under review) http://arxiv.org/abs/1603.02580
Notes: - Dynamic Power of add instruction in mW
Hamming weight of output datapath in number of bits set
Dynamic power in mW for add instruction, with output datapath cost subtracted (assuming 4.4mW per bit)
Hamming weight of both input operands to an add instruction, in number of bits set
Dynamic power in mW with input datapath cost subtracted (assuming 1.3mW per bit)
Dynamic power in mW with output and input datapath costs subtracted

## Slide 70: Energy Consumption Analysis enables energy transparency
www.theguardian.com

## Slide 71
http://us.123rf.com/450wm/kentoh/kentoh1006/kentoh100600301/7129999-futuristic-technology-data-flow-as-art-background.jpg
www.theguardian.com
Energy Consumption Analysis enables energy transparency

## Slide 72: SRA at the ISA Level
Combine static resource analysis (SRA) with the ISA-level energy model.
Provide energy consumption function parameterised by some property of the program or its data.

## Slide 73
Static Energy Usage Analysis
int fact (int x) {
if (x<=0)a
return 1b;
return (x *d fact(x-1))c;
}
Cfact(x) = Ca + Cb if x<=0
Cfact(x) = Ca + Cc(x) if x>0
Cc(x) = Cd + Cfact(x-1)
Substitute Ca, Cb, Cd with
the actual energy required to execute the corresponding lower-level (machine) instructions.
Solve equation using off-the-shelf solvers.
Result: Cfact(x) = (26x + 19.4) nJ
Original Program:
Extracted Cost Relations:
73

## Slide 74: ISA-Level Analysis Results
U. Liqat, S. Kerrison, A. Serrano, K. Georgiou, N. Grech, P. Lopez-Garcia, M.V. Hermenegildo and K. Eder. “Energy Consumption Analysis of Programs based on XMOS ISA-Level Models”. LOPSTR 2013.

## Slide 75: ISA-Level Analysis Results
U. Liqat, S. Kerrison, A. Serrano, K. Georgiou, N. Grech, P. Lopez-Garcia, M.V. Hermenegildo and K. Eder. “Energy Consumption Analysis of Programs based on XMOS ISA-Level Models”. LOPSTR 2013.

## Slide 76: Analysis Options
76
Moving away from the underlying model risks loss of accuracy.
But it brings us closer to the original source code.
Notes: A larger class of programs can be analyzed at LLVM IR level than at ISA level, because the LLVM IR level retains a lot of information on code structure and typing, which is lost at the ISA level.

## Slide 77: Energy Consumption of LLVM IR
U. Liqat, K. Georgiou, S. Kerrison, P. Lopez-Garcia, J.P. Gallagher, M.V. Hermenegildo, K. Eder. Inferring Parametric Energy Consumption Functions at Different Software Levels: ISA vs. LLVM IR. In Proceedings of FOPARA 2015. http://arxiv.org/abs/1511.01413
K. Georgiou, S. Kerrison and K. Eder, Oct 2015. “On the Value and Limits of Multi-level Energy Consumption Static Analysis for Deeply Embedded Single and Multi-threaded Programs”. http://arxiv.org/abs/1510.07095

## Slide 78: Analysis at the LLVM-IR Level
N. Grech, K. Georgiou, J. Pallister, S. Kerrison, J. Morse, K. Eder. 2015. Static analysis of energy consumption for LLVM IR programs. In Proceedings of the 18th International Workshop on Software and Compilers for Embedded Systems (SCOPES '15). ACM, New York, NY, USA, pages 12-21. http://dx.doi.org/10.1145/2764967.2764974

## Slide 79: EC Static Analysis Results
K. Georgiou, S. Kerrison and K. Eder, Oct 2015. “On the Value and Limits of Multi-level Energy Consumption Static Analysis for Deeply Embedded Single and Multi-threaded Programs”. http://arxiv.org/abs/1510.07095

## Slide 80: EC Static Analysis Results
K. Georgiou, S. Kerrison and K. Eder, Oct 2015. “On the Value and Limits of Multi-level Energy Consumption Static Analysis for Deeply Embedded Single and Multi-threaded Programs”. http://arxiv.org/abs/1510.07095

## Slide 81: EC Static Analysis Results
K. Georgiou, S. Kerrison and K. Eder, Oct 2015. “On the Value and Limits of Multi-level Energy Consumption Static Analysis for Deeply Embedded Single and Multi-threaded Programs”. http://arxiv.org/abs/1510.07095

## Slide 82: Towards Energy Aware Software Engineering

## Slide 83: Energy Transparency
83
For HW designers:
“Power is a 1st and last order design constraint.”
[Dan Hutcheson, VLSI Research, Inc., E3S Keynote 2011]
“Every design is a point in a 2D plane.”
[Mark Horowitz,E3S 2009]

## Slide 84: Energy Transparency
84
For HW designers:
“Power is a 1st and last order design constraint.”
[Dan Hutcheson, VLSI Research, Inc., E3S Keynote 2011]
“Every design is a point in a 2D plane.”
[Mark Horowitz,E3S 2009]

## Slide 85: Energy Transparency
85
For HW designers:
“Power is a 1st and last order design constraint.”
[Dan Hutcheson, VLSI Research, Inc., E3S Keynote 2011]
“Every design is a point in a 2D plane.”
[Mark Horowitz,E3S 2009]

## Slide 86: Energy Transparency
86
For HW designers:
“Power is a 1st and last order design constraint.”
[Dan Hutcheson, VLSI Research, Inc., E3S Keynote 2011]
“Every design is a point in a 2D plane.”
[Mark Horowitz,E3S 2009]

## Slide 87: More POWER to SW Developers
Full Energy Transparency
from HW to SW
Location-centric programming model
87
    in 5pJ do {...}
“Cool” code for green software
A cool programming competition!
Promoting energy efficiency
to a 1st class SW design goal is an
urgent research challenge.
Pictures taken from the Energy Efficient Computing Brochure at: https://connect.innovateuk.org/documents/3158891/9517074/Energy%20Efficient%20Computing%20Magazine?version=1.0
Notes: For decades, moved SW dev away from HW – need to bridge the gap!
Location-centric programming to expose cost of communication to developers 

## Slide 88: EACO @ Bristol
The Energy-Aware COmputing Initiative, Research Agenda and Workshops
http://www.cs.bris.ac.uk/Research/Micro/eaco.jsp

## Slide 89: EACO Research at Bristol
EACO Platform
  Online power monitoring
  RTOS API
EACOF (github.com/eacof)
  API for SW energy measurement
Machine Guided Energy Efficient Compilation (MAGEEC)
Superoptimization for low energy
Whole Systems Energy Transparency (ENTRA)
Layout
RTL / micro-architecture
Synthesis
Functional Blocks
Gate
Compiler
Program
Algorithms
Application
ISA
OS

## Slide 90: The ICT-Energy CSA
http://www.ict-energy.eu/
Notes: link to video at www.ict-energy.eu
OR
ICT-Energy project.mp4 file locally

## Slide 92: ICT-Energy Summer School
  Basic on the physics of energy transformations at micro and nanoscales
  Introduction to energy harvesting and distributed autonomous mobile devices
  Software and energy aware computing
  High performance computing and systems
13-16 August 2016
Aalborg, DK
Topics:
http://www.nipslab.org/summerschool2016

## Slide 93: ICT Energy Summer School
13-16 August 2016, Aalborg
Notes: … now getting ready for H2020 call in April
this time we are contributing towards setting the Strategic Research Agenda ;)
SRA in ICT-Energy CSA 

## Slide 94: ICT-Energy Science Conference
1st International Conference on ICT-Energy
16-19 August 2016, Aalborg, DK
  Session I: Fundamental limits in energy consumption of computing
  Session II: Novel architectures and devices for energy efficient computing
  Session III: Efficient Energy harvesting for autonomous devices
  Session IV: Energy aware software
  Session V: HPC energy constrains towards exascale computers
http://www.ict-energy.eu/scienceconference_home
Notes: … now getting ready for H2020 call in April
this time we are contributing towards setting the Strategic Research Agenda ;)
SRA in ICT-Energy CSA 

## Slide 95: ICT-Energy Strategic Research Roadmap
http://www.ict-energy.eu/sites/ict-energy.eu/files/ICTEnergySRA5.3.pdf
Notes: … now getting ready for H2020 call in April
this time we are contributing towards setting the Strategic Research Agenda ;)
SRA in ICT-Energy CSA 

## Slide 96
Thank you for your attention
Kerstin.Eder@bristol.ac.uk

## Slide 98
98
If you want an ultimate low-power system, then you have to worry about energy usage at every level in the system design, and you have to get it right from top to bottom, because any level at which you get it wrong is going to lose you perhaps an order of magnitude in terms of power efficiency.
The hardware technology has a first-order impact on the power efficiency of the system, but you've also got to have software at the top that avoids waste wherever it can. You need to avoid, for instance, anything that resembles a polling loop because that's just burning power to do nothing.
I think one of the hard questions is whether you can pass the responsibility for the software efficiency right back to the programmer.
Do programmers really have any understanding of how much energy their algorithms consume?
I work in a computer science department, and it's not clear to me that we teach the students much about how long their algorithms take to execute, let alone how much energy they consume in the course of executing and how you go about optimizing an algorithm for its energy consumption.
Some of the responsibility for that will probably get pushed down into compilers, but I still think that fundamentally, at the top level, programmers will not be able to afford to be ignorant about the energy cost of the programs they write.
What you need in order to be able to work in this way at all is instrumentation that tells you that running this algorithm has this kind of energy cost and running that algorithm has that kind of energy cost.
You need tools that give you feedback and tell you how good your decisions are. Currently the tools don't give you that kind of feedback.
February 2010, acmqueue Interview with Steve Furber
The designer of the ARM chip shares lessons on energy-efficient computing at: http://queue.acm.org/detail.cfm?id=1716385
Steve Furber
Notes: acmqueue> We've focused a lot on the hardware, and I think that's a very important
context in the framework of what's going on with energy and computing. Looking
forward, is most of this pursuit to be energy efficient going to be achieved by
advances in the component and hardware technology, or is it also going to have
great consequence for software developers?
98

## Slide 99
99
If you want an ultimate low-power system, then you have to worry about energy usage at every level in the system design, and you have to get it right from top to bottom, because any level at which you get it wrong is going to lose you perhaps an order of magnitude in terms of power efficiency.
The hardware technology has a first-order impact on the power efficiency of the system, but you've also got to have software at the top that avoids waste wherever it can. You need to avoid, for instance, anything that resembles a polling loop because that's just burning power to do nothing.
I think one of the hard questions is whether you can pass the responsibility for the software efficiency right back to the programmer.
Do programmers really have any understanding of how much energy their algorithms consume?
I work in a computer science department, and it's not clear to me that we teach the students much about how long their algorithms take to execute, let alone how much energy they consume in the course of executing and how you go about optimizing an algorithm for its energy consumption.
Some of the responsibility for that will probably get pushed down into compilers, but I still think that fundamentally, at the top level, programmers will not be able to afford to be ignorant about the energy cost of the programs they write.
What you need in order to be able to work in this way at all is instrumentation that tells you that running this algorithm has this kind of energy cost and running that algorithm has that kind of energy cost.
You need tools that give you feedback and tell you how good your decisions are. Currently the tools don't give you that kind of feedback.
February 2010, acmqueue Interview with Steve Furber
The designer of the ARM chip shares lessons on energy-efficient computing at: http://queue.acm.org/detail.cfm?id=1716385
Steve Furber
Notes: acmqueue> We've focused a lot on the hardware, and I think that's a very important
context in the framework of what's going on with energy and computing. Looking
forward, is most of this pursuit to be energy efficient going to be achieved by
advances in the component and hardware technology, or is it also going to have
great consequence for software developers?
99